## Slide 1
Decoder Start
Decoder Initialization & Preprocessing
Feed Forward Processing
If not inputs data ended
Traceback Processing
Decoder
End
Next set of inputs
False
True

## Slide 2
Initialization Start
Defined required parameters
Foreach possible states
Initialization End
Foreach possible inputs
Fill in input table
Fill in next state table
Fill in output table
End of possible states
End of possible inputs
Decoder Initialization & Preprocessing Unit

## Slide 3
Feed Forward Start
Foreach possible states
Feed Forward End
Foreach possible inputs
Obtain the binary outputs based on current state and current input
Compute the branch metric.
Save an accumulated metric value for the survivor state.
End of possible states
End of possible inputs
Feed Forward Processing Unit
Update the state history array with the state number of the survivor.

## Slide 4
Traceback Start
If t >= trellis depth - 1
Traceback End
Find the element of state history with the minimum accum. error metric
Traceback Processing Unit
Work backwards from the end of the trellis to the oldest state in the trellis to determine the optimal path.
Compute the input sequence corresponds to the state sequence in the optimal path
False
True

## Slide 5
vdsim.h
Viterbi decoder simulation header file. Contains parameters and function prototype.
test.cpp
Main entry of the programme.
Control the flow of simulation environment.
Define the tests.
sdvd.cpp
Defines soft decision Viterbi decoder.
utils.cpp
Contain helper functions that are used in both decoder and encoder.
Test Environment
Design Space

## Slide 6
Table Construct Kernel
out

## Slide 7
Feed Forward Kernel
out
input_data
tables

## Slide 8
Traceback Kernel
decoder_output_matrix
input_data
tables